;**********************************************************************
; *
; FIR Filter - Coursework1 Filter 7 - Extended Solution *
; Implements interrupt-driven ADC sampling with GPIO output *
; Author: *
; Date: *
; *
;**********************************************************************

list	p=16f877A
#include	<p16f877A.inc>

   __CONFIG _CP_OFF & _WDT_OFF & _BODEN_OFF & _PWRTE_ON & _RC_OSC & _WRT_OFF & _LVP_ON & _CPD_OFF

;**************************************************************************
; MACROS
;**************************************************************************
;Shift a 16 bit value left (x2)
SHIFT_LEFT_16 MACRO lower_byte, upper_byte
   bcf	STATUS,C
   rlf	lower_byte,f
   rlf	upper_byte,f
   ENDM

;Shift a 16 bit value right (/2)
SHIFT_RIGHT_16 MACRO lower_byte, upper_byte
   bcf	STATUS,C
   rrf	upper_byte,f
   rrf	lower_byte,f
   ENDM

;Add 16 bit temporary values to accumulator
ADD_ACCUM MACRO
   movf	temp_lower,w
   Addwf	accum_lower,f
   btfsc	STATUS,C
   incf	accum_upper,f
   movf	temp_upper,w
   Addwf	accum_upper,f
   ENDM

;Negate a 16-bit signed value
TWOS_COMPLEMENT_16 MACRO lower_byte, upper_byte
   comf	lower_byte,f
   comf	upper_byte,f
   movlw	0x01
   addwf	lower_byte,f
   btfsc	STATUS,C
   incf	upper_byte,f
   ENDM

;Unscaling from Q2 format
UNSCALE_Q2 MACRO lower_byte, upper_byte
   SHIFT_RIGHT_16	lower_byte, upper_byte
   SHIFT_RIGHT_16	lower_byte, upper_byte
   ENDM

;Clear 16 bit register pair
CLEAR_16 MACRO lower_byte, upper_byte
   clrf	lower_byte
   clrf	upper_byte
   ENDM

;**************************************************************************
; Variable definations
;**************************************************************************

;Input Sample
x_k	EQU	0x20
x_k_lower	EQU	0x21
x_k_upper	EQU	0x22

;Delayed Samples (FIR filter delay line)
x_k1_lower	EQU	0x23
x_k1_upper	EQU	0x24
x_k2_lower	EQU	0x25
x_k2_upper	EQU	0x26
x_k3_lower	EQU	0x27
x_k3_upper	EQU	0x28
x_k4_lower	EQU	0x29
x_k4_upper	EQU	0x2A
x_k5_lower	EQU	0x2B
x_k5_upper	EQU	0x2C
x_k6_lower	EQU	0x2D
x_k6_upper	EQU	0x2E
x_k7_lower	EQU	0x2F
x_k7_upper	EQU	0x30

;Temporary Working Registers
temp_lower	EQU	0x31
temp_upper	EQU	0x32
temp2_lower	EQU	0x33
temp2_upper	EQU	0x34

;Accumulator
accum_lower	EQU	0x35
accum_upper	EQU	0x36

;Output
y_k	EQU	0x37

sample_flag	EQU	0x38 ;flag to indicate new ADC sample is ready

;Context Saving Variables for ISR
w_temp	EQU	0x7D	; variable used for context saving
status_temp	EQU	0x7E	; variable used for context saving
pclath_temp	EQU	0x7F	; variable used for context saving

;****************************************************************************
ORG 0x000	; processor reset vector
nop	; nop required for icd
goto main	; go to beginning of program

ORG 0x004	; Interrupt vector location

; Save context
movwf w_temp	; save off current W register contents
movf	STATUS,w	; move status register into W register
movwf	status_temp	; save off contents of STATUS register
movf	PCLATH,w	; move pclath register into w register
movwf	pclath_temp	; save off contents of PCLATH register

; Interrupt Service Routine Triggered by Timer0 overflow at 2kHz
; Acquires ADC sample and sets flag for main loop processing

; Read 8-bit ADC result from ADRESH (Bank 1)
bsf STATUS, RP0
movf ADRESH, w
bcf STATUS, RP0
movwf x_k	; Store ADC sample

bsf sample_flag, 0 ; Set flag to start main loop nwhen a sample is recieved

bsf ADCON0, GO ; Start next ADC conversion

movlw .6	; Reload Timer0 for consistent 2kHz sampling rate
movwf TMR0

bcf INTCON, T0IF ;Clear Timer0 interrupt flag

; Restore context
movf	pclath_temp,w
movwf	PCLATH
movf status_temp,w
movwf	STATUS
swapf w_temp,f
swapf w_temp,w
retfie
;****************************************************************************

main
; Configure PORTB as output for filter result
bsf STATUS, RP0	;Switch to Bank 1
clrf TRISB	;All PORTB pins as outputs
bcf STATUS, RP0	;Back to Bank 0
clrf PORTB	;Clear PORTB

; Configure ADC: AN0 as analog input, right-justified result
bsf STATUS, RP0
movlw b'10001110'	; Right justified, AN0 analog
movwf ADCON1
bcf STATUS, RP0

movlw b'01000001'	; Fosc/8 clock speed with AN0 selected and ADC enabled
movwf ADCON0

; Configure Timer0 for 2kHz interrupt rate
bsf STATUS, RP0
movlw b'00000000'	; Internal clock, prescaler 1:2 = 2kHz
movwf OPTION_REG
bcf STATUS, RP0

movlw .6	; Preload value for 2kHz
movwf TMR0
bsf INTCON, T0IE	; Enable Timer0 interrupt
bsf INTCON, GIE	; Enable global interrupts

bsf ADCON0, GO ; Start first ADC conversion

; Initialize all filter registers to zero
clrf	x_k
CLEAR_16 x_k_lower, x_k_upper
CLEAR_16 x_k1_lower, x_k1_upper
CLEAR_16 x_k2_lower, x_k2_upper
CLEAR_16 x_k3_lower, x_k3_upper
CLEAR_16 x_k4_lower, x_k4_upper
CLEAR_16 x_k5_lower, x_k5_upper
CLEAR_16 x_k6_lower, x_k6_upper
CLEAR_16 x_k7_lower, x_k7_upper
CLEAR_16 accum_lower, accum_upper
clrf	y_k
clrf	sample_flag

Sample_loop

btfss	sample_flag, 0 ; Wait for new ADC sample from ISR
goto	Sample_loop

bcf	sample_flag, 0 ; when flag is set upon completion of a interrupt

;Process Input
call	PROCESS_INPUT
call	SCALE_INPUT

CLEAR_16 accum_lower, accum_upper ; Clear Accumulator

; Run all the MAC operations
call	TAP_1
call	TAP_2
call	TAP_3
call	TAP_4
call	TAP_5
call	TAP_6
call	TAP_7

; Unscale result
UNSCALE_Q2 accum_lower, accum_upper

; Store result into y_k
movf	accum_lower,w
movwf	y_k

; Output result to PORTB
movf	y_k,w
movwf	PORTB

; Update delay line
call	UPDATE_DELAY_LINE

goto	Sample_loop	; Wait for next sample

;**************************************************************************
; Subroutines
;**************************************************************************

;Processing input - Sign extension and Scaling
PROCESS_INPUT
movf	x_k,0	;Loading the 8 bit value to W register
movwf	x_k_lower	;Store into lower byte of 16 bit value

btfsc	x_k_lower,7	;Check MSB (bit 7) - skip if bit 7 is 0
goto	NEGATIVE_INPUT	;Bit 7 is 1
goto	POSITIVE_INPUT	;Bit 7 is 0
NEGATIVE_INPUT
movlw	0xFF	; ;Load 0xFF
movwf	x_k_upper	;Upper byte for negative numbers set as 0XFF
return
POSITIVE_INPUT
clrf	x_k_upper	;Clear Upper byte for positive numbers
return

;Scaled from Q0 to Q2 (x4) - two fractional bits
SCALE_INPUT
SHIFT_LEFT_16 x_k_lower, x_k_upper	; x2
SHIFT_LEFT_16 x_k_lower, x_k_upper	; x2 again = x4
return

;Arithmic Overflow check
OVERFLOW
BTFSS	accum_upper,7	;Test bit 7
goto	POSITIVE	;If clear the value is positive
NEGATIVE
BTFSS	accum_upper,6	;Test bit 6
goto	NEG_OVERFLOW_SAT	;If clear negative overflow ocurred
return
POSITIVE
BTFSC	accum_upper,6	;Test bit 6
goto	POS_OVERFLOW_SAT	;If set positive overflow ocurred
return
NEG_OVERFLOW_SAT
movlw	0X80	;Upper byte -32768 : (1000 0000)
movwf	accum_upper
movlw	0x00	;Lower byte -32768 : (0000 0000)
movwf	accum_lower
return
POS_OVERFLOW_SAT
movlw	0x7F	;Upper byte +32767 : (0111 1111)
movwf	accum_upper
movlw	0xFF	;Lower byte +32767 : (1111 1111)
movwf	accum_lower
return

;Shifting each sample down the delay line
UPDATE_DELAY_LINE
movf	x_k6_lower,w
movwf	x_k7_lower
movf	x_k6_upper,w
movwf	x_k7_upper

movf	x_k5_lower,w
movwf	x_k6_lower
movf	x_k5_upper,w
movwf	x_k6_upper

movf	x_k4_lower,w
movwf	x_k5_lower
movf	x_k4_upper,w
movwf	x_k5_upper

movf	x_k3_lower,w
movwf	x_k4_lower
movf	x_k3_upper,w
movwf	x_k4_upper

movf	x_k2_lower,w
movwf	x_k3_lower
movf	x_k2_upper,w
movwf	x_k3_upper

movf	x_k1_lower,w
movwf	x_k2_lower
movf	x_k1_upper,w
movwf	x_k2_upper

movf	x_k_lower,w
movwf	x_k1_lower
movf	x_k_upper,w
movwf	x_k1_upper
return

TAP_1
;Multiply: x (k-1) * 0.5 (Q2 scaled is x2)
movf	x_k1_lower,w	;Load Lower byte of x(k-1)
movwf	temp_lower	;Store in temp_lower
movf	x_k1_upper,w	;Load Upper byte of x(k-1)
movwf	temp_upper	;Store in temp_upper

;Multiply x2
SHIFT_LEFT_16 temp_lower, temp_upper

;Add x(k-1) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return

TAP_2
;Multiply: x(k-2) * 1.5 (Q2 scaled is x6)
movf	x_k2_lower,w	;Load lower byte of x(k-2)
movwf	temp_lower	;Store in temp_lower
movf	x_k2_upper,w	;Load upper byte of x(k-2)
movwf	temp_upper	;Store in temp_upper

movf	x_k2_lower,w	;Load lower byte of x(k-2)
movwf	temp2_lower	;Store in temp2_lower
movf	x_k2_upper,w	;Load upper byte of x(k-2)
movwf	temp2_upper	;Store in temp2_upper

;Multiply x4
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 1 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 2 (x2)

;Multiply x2
SHIFT_LEFT_16 temp2_lower, temp2_upper	;Shift 1 (x2)

;Addition of x4 and x2 values for x6
bcf	STATUS, C	;Clear Carry Flag
movf	temp2_lower,w	;Load x2 value lower byte
addwf	temp_lower,f	;Add x2 and x4 lower byte values
btfsc	STATUS,C	;If carry flag set, increment upper byte
incf	temp_upper,f

movf	temp2_upper,w	;Load x2 value upper byte
addwf	temp_upper,f	;Add x2 and x4 upper byte values

;Add x(k-2) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return

TAP_3
;Multiply: x(k-3) * 4 (Q2 scaled is x16)
movf	x_k3_lower,w	;Load Lower byte of x(k-3)
movwf	temp_lower	;Store in temp_lower
movf	x_k3_upper,w	;Load Upper byte of x(k-3)
movwf	temp_upper	;Store in temp_upper

;Multiply x16
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 1 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 2 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 3 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 4 (x2)

;Add x(k-3) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return

TAP_4
;Multiply: x(k-4) * 4 (Q2 scaled is x16)
movf	x_k4_lower,w	;Load Lower byte of x(k-4)
movwf	temp_lower	;Store in temp_lower
movf	x_k4_upper,w	;Load Upper byte of x(k-4)
movwf	temp_upper	;Store in temp_upper

;Multiply x16
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 1 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 2 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 3 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 4 (x2)

;Add x(k-4) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return

TAP_5
;Multiply: x(k-5) * 1.5 (Q2 scaled is x6)
movf	x_k5_lower,w	;Load lower byte of x(k-5)
movwf	temp_lower	;Store in temp_lower
movf	x_k5_upper,w	;Load upper byte of x(k-5)
movwf	temp_upper	;Store in temp_upper

movf	x_k5_lower,w	;Load lower byte of x(k-5)
movwf	temp2_lower	;Store in temp2_lower
movf	x_k5_upper,w	;Load upper byte of x(k-5)
movwf	temp2_upper	;Store in temp2_upper

;Multiply x4
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 1 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 2 (x2)

;Multiply x2
SHIFT_LEFT_16 temp2_lower, temp2_upper	;Shift 1 (x2)

;Addition of x4 and x2 values for x6
bcf	STATUS, C	;Clear Carry Flag
movf	temp2_lower,w	;Load x2 value lower byte
addwf	temp_lower,f	;Add x2 and x4 lower byte values
btfsc	STATUS,C	;If carry flag set, increment upper byte
incf	temp_upper,f

movf	temp2_upper,w	;Load x2 value upper byte
addwf	temp_upper,f	;Add x2 and x4 upper byte values

;Add x(k-5) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return

TAP_6
;Multiply: x(k-6) * 2 (Q2 scaled is x8)
movf	x_k6_lower,w	;Load Lower byte of x(k-6)
movwf	temp_lower	;Store in temp_lower
movf	x_k6_upper,w	;Load Upper byte of x(k-6)
movwf	temp_upper	;Store in temp_upper

;Multiply x8
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 1 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 2 (x2)
SHIFT_LEFT_16 temp_lower, temp_upper	;Shift 3 (x2)

;Add x(k-6) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return

TAP_7
;Multiply: x(k-7) * (-0.25) (Q2 scaled is x-1)
movf	x_k7_lower,w	;Load Lower byte of x(k-7)
movwf	temp_lower	;Store in temp_lower
movf	x_k7_upper,w	;Load Upper byte of x(k-7)
movwf	temp_upper	;Store in temp_upper

;Twos Complement of x(k-7)
TWOS_COMPLEMENT_16 temp_lower, temp_upper

;Add -x(k-7) Accumulator
ADD_ACCUM

;Check Arithmetic overflow after accumulation
call	OVERFLOW
return
END